ITEM / CONSTRUCTION:     KERBSTONES AT PEDESTRIAN CROSSINGS	1

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street mileus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | No lateral inclination | Warning areas Guidance paving flags Pedestrian crossing signs Railings (guide railings) | Blister paving flags or warning areas always before vertical kerb Collision-prevention solutions at pedestrian crossing Min. width of vertical kerbstone 1,500 mm, perpendicular to carriageway At diagonal pedestrian crossings, direction is indicated by a strip of split-face stone paving flags (width 200-300 mm) at the edge of pedestrian crossing markings Ice and snow melting system recommended for blister paving flags and warning area For maintenance by machine, recommended width of ramp kerbstone 2,500 mm, functional minimum width 900 mm | In blister paving flags or warning areas, colour/contrast distinct from pavement surface (contrast requirement: difference between medium grey and black/white) Good lighting; glare-free, even. Recommended lighting intensity 20 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) Guidance lighting where necessary for persons who are partially sighted | Guidance/warning pattern to be readily recognisable Colour contrast to remain distinct Height of kerbstone to remain unchanged Ramp kerbstone to remain unchanged Prevention of puddle formation |
| 2 BASIC LEVEL OF ACCESSIBILITY |  | Warning area Pedestrian crossing signs Railings (guide railings) | Warning area installed, if basic level accessibility route has been rated important Collision-prevention solutions at pedestrian crossing Min. width of vertical kerbstone 1,500 mm perpendicular to carriageway At diagonal pedestrian crossings, direction is indicated by a strip of split-face stone paving flags (width 200-300 mm) at edge of pedestrian crossing markings For maintenance by machine, recommended width of ramp kerbstone 2,500 mm, functional minimum width 900 mm | In warning areas and at kerbsides, colour/contrast distinct from pavement surface recommended (contrast requirement: difference between medium grey and black/white) Street lighting in accordance with functional street classification Good lighting; glare-free, even | Height of kerbstone to remain unchanged Surface patterns to remain distinct |

ITEM / CONSTRUCTION:     OUTDOOR STAIRCASES	2

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Tread in heated staircases 390 mm Recommendation: intermediate landing every 10-15 steps Min. width 1,200 mm See: RakMK F2 (Safety specifications for buildings) | Ramps Warning areas Guidance paving flags Handrails Railings Colour/contrast strips | Recommended sizing for outdoor staircases: 2 x rise + tread = 660 mm (RT 88-10470, 1992) Sizing for covered and heated staircases: 2 x rise + tread = 630 mm Alternative stairless access always Ice and snow melting system recommended Rough surface, non-slippery when wet Warning area or blister paving flags always at top and bottom of staircase Colour/contrast strip at edge of steps. Contrast strip either part of structural solution of steps or grout filling in a cut groove Edge perpendicular to direction of travel Handrails at two heights always on both sides of staircase In wide staircases, handrails in the middle at intervals of 2,400 mm | At edge of steps, colour/contrast strip distinct from material of steps (contrast requirement: difference between medium grey and black/white), primarily a dark strip on a light step Light colouring of stairs to show shadows cast by steps Good lighting; glare-free, even. Recommended lighting intensity 50 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) Special stairway light where necessary | Ice and snow melting system to remain functional. If faulty, apply non-slip treatment. Clean, non-slippery surface Surface pattern and colour contrast of blister paving flags and warning areas to remain distinct At edge of steps, colour/contrast strip to remain distinct In heated steps, tread can be 375 mm Piling of snow under handrail prohibited. Vegetation to be kept from the steps. Vegetation must not hamper use of handrail. |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE Alternative method in renovation See: RakMK F2 (Safety specifications for buildings) | Ramps Handrails Railings Warning areas (strips) | Alternative stairless access always Rough surface, non-slippery when wet Acceptable alternative in renovation: Colour/contrast strip at edge of top and bottom step, also before and after intermediate landing Handrails always on both sides of staircase In wide staircases, handrails in the middle at intervals of 2,400 mm | At edge of steps, colour/contrast strip distinct from material of steps (contrast requirement: difference between medium grey and black/white), primarily a dark strip on a light step Light colouring of stairs to show shadows cast by steps Minimum lighting category K2 (min. 10 lux) Good lighting: glare-free, even | Non-slip treatment (sanding, etc.) Rough, non-slippery surface Colour/contrast strip of front edge of top step to remain distinct Piling of snow under handrail prohibited. Vegetation to be kept from the steps. Vegetation must not hamper use of handrail. Passage prohibited if there is no wintertime maintenance |

ITEM / CONSTRUCTION:     RAMPS	3

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Recommended inclination < 5% (< 1:20, c. 3º) Without intermediate landings, inclination max. 5% Lateral inclination max. 2% Width of ramp maintained by machine ≥ 2,300 mm Recommended width 1,200–1,800 mm (min. 900 mm) See: RakMK F1 (Specifications for accessible building construction) | Staircases Guidance paving flags Warning areas Handrails Walking surfaces | Warning area at top and bottom of ramp Handrails at two heights always on both sides at full length of ramp and intermediate landings Ice and snow melting system recommended Rough surface material, non-slippery in all weather conditions Protective edge (min. 50 mm) in the absence of a wall or other solid barrier at edge of ramp Landing at turning point of ramp (minimum size 1,150 x 1,150 mm) | In warning areas, distinct colour/contrast (contrast requirement: difference between medium grey and black/white) Good lighting; glare-free, even. Recommended lighting intensity 30 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) Guidance lighting where necessary for persons who are partially sighted | Non-slip treatment Surface pattern and colour contrast of warning area to remain distinct Piling of snow under handrail prohibited Vegetation to be kept from the ramp. Vegetation must not hamper use of handrail. |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE See: RakMK F1 (Specifications for accessible building construction) | Staircases Warning areas Handrails Walking surfaces | Ramp and staircase needed Handrails at two heights always on both sides at full length of ramp and intermediate landings Rough surface material, non-slippery in all weather conditions Protective edge (min. height 50 mm) in the absence of a wall or other solid barrier at edge of ramp | Minimum lighting category K2 (min. 10 lux) Good lighting: glare-free, even | Non-slip treatment Piling of snow under handrail prohibited. Vegetation to be kept from the ramp. Vegetation must not hamper use of handrail. |

ITEM / CONSTRUCTION:     GUIDANCE PAVING FLAGS	4

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | BLISTER PAVING FLAG: cupola pattern Width in direction of travel 1,200 mm, when going to staircase or ramp leading directly down; otherwise 600 mm DIRECTIONAL GUIDANCE PAVING FLAG: half-rod and bar patterns Half-rod and bar patterns installed in direction of travel | Kerbstone Outside staircases Ramps Loading islands Walking surfaces Railings (guide railings) | Guidance paving flags positioned to lead logically to destination To avoid misunderstanding, no other paving materials resembling these in colouring, surface pattern or texture are to be used nearby Ice and snow melting system or roof recommended Always consult experts at the Finnish Federation of the Visually Impaired or at Finlands Svenska Synskadade | Colour/contrast distinct from surface (contrast requirement: difference between medium grey and black/white), primarily light colouring Good lighting; glare-free, even. Recommended lighting intensity 20 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) Light possibly integrated in guidance/warning pattern | Guidance and warning pattern to remain distinct Colour contrast to remain distinct |
| 2 BASIC LEVEL OF ACCESSIBILITY |  |  |  |  |  |

ITEM / CONSTRUCTION:     DEMARCATION STRIPS   Segregated pedestrian footpaths and cycle paths; demarcation strips at kerbside	5

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. |  | Warning areas Walking surfaces Railings Bollards | Material: setts of split-face small natural stone To avoid misunderstanding, no other paving materials resembling these in colouring, surface pattern or texture are to be used nearby Surfaces that are functionally distinguished (for instance pedestrian footpaths and cycle paths): use of differing materials and colours recommended Demarcation strip (min. width 500 mm) recommended at the kerbside, when the pavement adjoins the carriageway | Colour/contrast distinct from surface (contrast requirement: difference between medium grey and black/white) Minimum lighting category K2, min 10 lux Good lighting; glare-free, even | Surface patterns of demarcation strips to be distinct in all weather conditions Colour contrast to remain distinct |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE Gunning | Walking surfaces Railings Bollards | INSTRUCTIONS AS ABOVE | Colour/contrast distinct from surface (contrast requirement: difference between medium grey and black/white) Street lighting in accordance with functional street classification | Surface patterns of demarcation strips to be distinct in all weather conditions Colour contrast to remain distinct |

ITEM / CONSTRUCTION:     LOADING ISLANDS	6

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Raised level bus stops | Walking surfaces Guidance paving flags Warning areas Public transport stop poles Tactile signs | To avoid misunderstanding, no other paving materials resembling warning areas in colouring, surface pattern or texture are to be used nearby Pavement materials limited to those agreed on for or used in the neighbourhood Detailed planning instructions: Suraku Instruction Card 7, and City of Helsinki Public Works Department, Type Drawing 2007: 29263/10 ”Esteettömyyden erikoistason pysäkkisyvennys”; 29263/11 “Ajoratapysäkki” www.hel.fi/helsinkikaikille/ | In warning areas: colour/contrast clearly distinguished from pavement/surface (contrast requirement: difference between medium grey and black/white) Good lighting; glare-free, even. Recommended lighting intensity 20 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) | Surface patterns of warning area to be distinct in all weather conditions Non-slip treatment |
| 2 BASIC LEVEL OF ACCESSIBILITY | Raised-level bus stops, INSTRUCTIONS AS ABOVE Street-level bus stops | Walking surfaces Warning areas Public transport bus stop poles | To avoid misunderstanding, no other paving materials resembling warning areas in colouring, surface pattern or texture are to be used in the neighbourhood Pavement materials limited to those agreed on for or used in the neighbourhood Detailed planning instructions: Suraku Instruction Card 7, and City of Helsinki Public Works Department, Type Drawing 2007: 29263/9 Esteettömyyden perustason pysäkkisyvennys, 29263/11 Ajoratapysäkki www.hel.fi/helsinkikaikille/ | In warning areas: colour/contrast clearly distinguished from pavement/surface (contrast requirement: difference between medium grey and black/white) Street lighting in accordance with functional street classification Good lighting; glare-free, even | Surface patterns of warning areas to be distinct in all weather conditions Non-slip treatment |

ITEM / CONSTRUCTION:     GUTTERS AND GULLIES	7

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Covered gutter, if depth > 20 mm Open gutter See: KT-02 (General Working Instructions for Municipal Engineering) | Walking surfaces Rainwater gullies Guidance paving flags Demarcation strips | Logically positioned in longitudinal direction of streets, thus helping to guide persons who are partially sighted Ice and snow melting system recommended Sufficient number of grate-covered rainwater gullies to prevent puddle formation Easy to clean | Colour or material distinct from surface | Keeping gutters open, prevention of icing, regular cleaning (removal of sand and rubbish) |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE | Walking surfaces Rainwater gullies Demarcation strips | Logically positioned in longitudinal direction of streets, thus helping to guide persons who are partially sighted Sufficient number of grate-covered rainwater gullies to prevent puddle formation Easy to clean | Colour or material distinct from surface | Keeping gutters open, prevention of icing, regular cleaning (removal of sand and rubbish) |

ITEM / CONSTRUCTION:     WALKING SURFACES	8

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Evenness of surfaces - deviation max. 5 mm per 2 metres - tile offset max. 5 mm - joint width max. 5 mm Longitudinal inclination - max. 5% Lateral inclination - max. 2% Slipperiness - hard surface - rough, non-slippery surface Width of path min. 900 mm See: KT-02 (General Working Instructions for Municipal Engineering) | Staircases Ramps Guidance paving flags Demarcation strips Rainwater gutters Rainwater gullies Pedestrian crossing markings | No structures that increase risk of stumbling or tripping Overhanging obstructions at minimum height of 2,200 mm; 3,000 mm for structures requiring planning permission Distinct contrast zone round obstructions | Minimum lighting category K2 (min. 10 lux) Good lighting; glare-free, even In functionally different areas (e.g. pedestrian footpaths and cycle paths) different colour or surface structure Light-coloured surfaces, and patterns facilitating route recognition. Patterns not to give the false impression of a staircase. | Securing evenness and serviceability of surfacing Non-slip treatment |
| 2 BASIC LEVEL OF ACCESSIBILITY | Evenness of surface, INSTRUCTIONS AS ABOVE Longitudinal inclination - max. 8% Lateral inclination - max. 3% Slipperiness - hard or medium-hard surface - rough, non-slippery surface See: KT-02 (General Working Instructions for Municipal Engineering) | Staircases Ramps Demarcation strips Rainwater gutters Rainwater gullies Pedestrian crossing markings | No structures that increase risk of stumbling or tripping Overhanging obstructions at minimum height of 2,200 mm; 3,000 mm for structures requiring planning permission | Street lighting in accordance with functional street classification Light surfaces, and patterns facilitating route recognition. Patterns not to give the false impression of a staircase. | Securing evenness and serviceability of surfacing Non-slip treatment |

ITEM / CONSTRUCTION:     PEDESTRIAN CROSSING MARKINGS	9

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Cycle path See: Resolution of the Ministry of Transport and Communications on Traffic Control Devices, Ch. 3, Sect. 31 See: KT-02 (General Working Instructions for Municipal Engineering) | Kerbstone Guidance paving flags Warning areas Walking surfaces Railings (guide railings) Pedestrian push-button posts Pedestrian crossing signs | No other similarly patterned surfaces nearby that are likely to cause misunderstandings Recommendation: Pedestrian crossing perpendicular to carriageway; and in any case perpendicular to the kerbstone At diagonal pedestrian crossings, direction is indicated by a strip of split-face stone paving flags (width 200-300 mm) at edge of pedestrian crossing markings Alternative materials: sawn natural stone (flamed or bush-hammered) cast stone gunning | White stripes in pedestrian crossings, dark street surface, maximum contrast (minimum contrast requirement: difference between medium grey and black/white) Good lighting; glare-free, even. Recommended lighting intensity 30 lux (”Unobstructed lighting and clear contrasts in station areas”; “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) | Patterns and colour contrast of pedestrian crossings to remain distinct Non-slip treatment |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE | Kerbstone Walking surfaces Railings (guide railings) Pedestrian push-button posts Pedestrian crossing signs | No other similarly patterned surfaces nearby that are likely to cause misunderstandings Recommendation: Pedestrian crossing perpendicular to carriageway and in any case perpendicular to the kerbstone At diagonal pedestrian crossings, direction is indicated by a strip of split-face stone paving flags (width 200-300 mm) at edge of pedestrian crossing markings Alternative materials: sawn natural stone (flamed or bush-hammered) cast stone gunning | White stripes in pedestrian crossings, dark street surface, maximum contrast (minimum contrast requirement: difference between medium grey and black/white) Street lighting in accordance with functional street classification | Patterns and colour contrast of pedestrian crossings to remain distinct Non-slip treament |

ITEM / CONSTRUCTION:     HANDRAILS	10

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | See: RakMK F2 (Safety specifications for buildings) See: KT-02 (General Working Instructions for Municipal Engineering) | Outside staircases Ramps Guidance paving flags Warning areas Walking surfaces Railings | Staircases and ramps: Handrails always at two heights on both sides (intermediate landings included) In wide staircases, handrails in the middle at intervals of 2,400 mm To prevent risk of collision or of clothes being caught in the handrail, the upper and lower handrails must be integrated, or bent down or sideways Staircase or ramp guide railing, where necessary Open railing to separate pram slope from staircase | Colour or material distinct from surroundings Guidance lighting, or rail lighting, where necessary for persons who are partially sighted | Handrail must be functional and in place at all times. Good working order must be ensured by temporary arrangements before replacing a damaged handrail. Piling of snow under handrail prohibited. Vegetation to be kept from the steps. Vegetation must not hamper use of handrail. Handrails must be smooth; wooden handrails must be free of splinters |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE See: RakMK F2 (Safety specifications for buildings) | Outside staircases Ramps Warning areas Walking surfaces Railings | Handrails always on both sides of staircase and ramp (intermediate landings included) In wide staircases, handrails in the middle at intervals of 2,400 mm Open railing to separate pram slope from staircase To prevent risk of collision or of clothes being caught in the handrail, the upper and lower handrails must be integrated, or bent down or sideways | Colour or material distinct from surroundings | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     RAILINGS	11

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Protective railing 1,200 mm, when difference in height > 6,000 mm 1,000 mm, when difference in height > 3,000 mm 900 mm, when difference in height > 700 mm Height of protective structure 900 mm, when height of railing 1,200 mm; otherwise 700 mm Open railing when difference in height > 500 mm, but not > 700 mm Applies also when difference in height is less, if there is a risk of tripping Collision barrier Used as middle handrail in staircases Used to separate pram slope from staircase | Outside staircases Ramps Handrails Bollards | No sharp edges or components causing risk of collision or of clothes being caught in railing Guiderail, if there is service traffic or other motor traffic at upper level Splash shield if railing in underpass For more details, see: RakMK F2 (Safety specifications for buildings) | Guidance lighting where necessary for persons who are partially sighted Safety colours in areas with motor traffic where necessary | Protection by handrail must be ensured at all times. Good working order must be ensured by temporary arrangements before replacing a damaged handrail. Handrail must be within easy reach, if railing includes handrail. Handrails must be smooth; wooden handrails must be free of splinters |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE Open railing possible in staircases with less than 3 steps | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     PEDESTRIAN PUSH-BUTTON POSTS 	12

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and the persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Push-button distinctly raised (tactile) See: Resolution of the Ministry of Transport and Communications on Traffic Lights in Road Traffic | Kerbstone Guidance paving flags Warning areas Pedestrian crossing markings Pedestrian crossing posts | Sound signal, where necessary At diagonal pedestrian crossings, indication of direction | Signal light in push-button | Push-button must function and be easily reached in winter |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE See: Resolution of the Ministry of Transport and Communications on Traffic Lights in Road Traffic | Kerbstone Warning areas Pedestrian crossing markings Pedestrian crossing posts | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     PEDESTRIAN CROSSING SIGNS	13

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Placed by pedestrian crossing markings at edge of carriageway/pavement Posts on both sides of pedestrian crossing, if street has 2 lanes See: Resolution of the Ministry of Transport and Communications on Traffic Control Devices, Ch. 2, Sect. 21 See: RT Building Information Card 98-10565 | Kerbstone Guidance paving flags Warning areas Demarcation strips Pedestrian crossing markings Pedestrian push-button posts | Standard placement of post important, as it helps people who are partially sighted in locating pedestrian crossings | Colour of post: light grey Safety colour stripe, where necessary | Post in good repair and readily recognisable |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE Placed by pedestrian crossing markings; max. distance from pedestrian crossing markings or cycle path markings: 2 m Distance from edge of carriageway max. 2 m (max. 3.5 m, if visibility good) See: Resolution of the Ministry of Transport and Communications on Traffic Control Devices, Ch. 2, Sect. 21 | Kerbstone Warning areas Demarcation strips Pedestrian crossing markings Pedestrian push-button posts | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     SEATING	14

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Recommended measurements in locations requiring special accessibility and along accessible routes Armrest always; in some benches only in the middle Backrest always Minimum distance between benches 50 m In addition to benches, resting places must be furnished with seats of varying heights and types See: Measurement recommendations of the Finnish Rheumatism Association | Warning areas Walking surfaces | No sharp components or structures; no components or structures causing collision or other risk; front edge of seat rounded Placed in furniture zone with readily recognisable surface Hard base surface material Placed outside path At one end of bench, adjoining space (min. 900 mm) for wheelchair, pram, etc. Recommendation: to make bench immovable, fasten to ground | Colour or material distinct from surroundings Minimum lighting category K2 (min. 10 lux) Good lighting; glare-free, even | Bench must be accessible under changing conditions, including wintertime Bench maintenance to ensure: cleanliness tidiness smoothness of surfaces |
| 2 BASIC LEVEL OF ACCESSIBILITY | Seat height 400–500 mm Armrest and backrest in at least some benches Backrest recommended Distance between benches according to need | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | Lighting in conformity with functional classification of environment | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     BOLLARDS IN PEDESTRIAN ZONES	15

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and disabled Areas with a lot of housing targeted at the elderly and the disabled Residential areas with special housing for the elderly, disabled, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | The bollard in the picture is just an illustration; the type of bollard is chosen in connection with the overall planning | Warning areas | No sharp edges or components causing risk of collision or of clothes being caught in bollards Readily recognisable surface material in bollard zone Recommended height 900 mm | Colour or material distinct from surroundings Reflecting stripe or section in bollard, if bollard is dark in colour Safety colour where necessary Bollard lighting where necessary | Recognisability of warning pattern must be guaranteed Sufficient colour contrast must be maintained. Safety colours must also be preserved. |
| 2 BASIC LEVEL OF ACCESSIBILITY |  | INSTRUCTIONS AS ABOVE | Height 600–900 mm | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     PEDESTRIAN REFUGE ISLANDS	16

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street environments City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Measurements consistent with ends of pedestrian crossings | Kerbstone Guidance paving flags Walking surfaces Pedestrian crossing markings Warning areas Pedestrian push-button posts Pedestrian crossing signs | See Accessibility Criteria 1: ”Kerbstones at Pedestrian Crossings” | Good lighting; glare-free, even. Recommended lighting intensity 20 lux (”Unobstructed lighting and clear contrasts in station areas”, “ELSA”, Ministry of Transport and Communications' Research and Development Programme for Accessibility) | Surface pattern and colour contrast of guidance paving flags and warning area to remain distinct |
| 2 BASIC LEVEL OF ACCESSIBILITY |  | Kerbstone Walking surfaces Pedestrian crossing markings Warning areas Pedestrian push-button posts Pedestrian crossing signs |  | Street lighting in accordance with functional street classification | INSTRUCTIONS AS ABOVE |

ITEM / CONSTRUCTION:     TACTILE MAPS AND INFORMATION SIGNBOARDS	17

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | RT Building Information Card 09-10884 RT Building Information Card 98-10565 | Guidance paving flags Railings (guide railings) | Typeface size 25–40 mm, if access to signboard unobstructed; 70-100 mm, if signboard is looked at from a distance of 1-3 metres To avoid risk of collision, mount signboard on base whose front edge is flush with signboard Recommendation: place tactile information and Braille texts in maps and signboards horizontally at an angle at a height of 900 mm Recommendation: provide overhead covering for signboard Always consult specialists at the Finnish Federation of the Visually Impaired or at Finlands Svenska Synskadade | Sufficient colour contrast; minimum 50% tone difference between text and background, also between signboard and background Best legibility: combination of black and white Minimum lighting category K2 Good lighting; glare-free, even, sufficient Lighting where necessary | Free access to signboard (arm’s reach) Guidance paving flags must remain readily recognisable Sufficient colour contrast must be maintained |
| 2 BASIC LEVEL OF ACCESSIBILITY |  |  |  |  |  |

ITEM / CONSTRUCTION:     WARNING AREAS	18

| ACCESSIBILITY REQUIREMENTS | MEASUREMENTS | ITEMS REQUIRING SPECIAL PLANNING ATTENTION See separate instructions | PLANNING INSTRUCTIONS | COLOURS AND LIGHTING | MAINTENANCE REQUIREMENTS |
| --- | --- | --- | --- | --- | --- |
| 1 SPECIAL LEVEL OF ACCESSIBILITY Pedestrian street milieus City centre areas with public facilities and services Areas surrounding institutions providing health care and services for the elderly and persons with a disability Areas with a lot of housing targeted at the elderly and persons with a disability Residential areas with special housing for the elderly, persons with a disability, etc. Public transport terminals and areas surrounding public bus stops Special sports areas and playgrounds Accessible routes in recreational areas, etc. | Width in direction of travel 1,200 mm, when going to staircase leading directly down; otherwise 600 mm | Kerbstone Outside staircases Ramps Guidance paving flags Demarcation strips Loading islands | Used to warn of edges, platforms, ramps, staircases, pedestrian crossings, etc., in the absence of blister paving flags. Alternative materials: • white natural stone paving flags (bush-hammered or fired) • white sawn stone setts (bush-hammered or fired) • white exposed-aggregate concrete paving flags • white concrete paving flags • white blister paving flags (ice and snow melting system installed in the area) To avoid misunderstanding, no other paving materials resembling these in colouring, surface pattern or texture are to be used nearby | Colour/contrast distinct from surface (minimum contrast requirement: difference between medium grey and black/white) Minimum lighting category K2, min. 10 lux Good lighting; glare-free, even | Recognisability of warning pattern must be guaranteed Sufficient colour contrast must be maintained |
| 2 BASIC LEVEL OF ACCESSIBILITY | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | INSTRUCTIONS AS ABOVE | Street lighting in accordance with functional street classification | INSTRUCTIONS AS ABOVE |